## Slide 1: Development of sub-ns GW peak power Nd:YAG laser system at 266nm for UV filament research
Xiaozhen Xu, Chengyong Feng
and Jean-Claude Diels
Department of Physics and Astronomy &
Center for High Tech Materials
The University of New Mexico

## Slide 2: Outline
Project Goal
Introduction of pulse compression through Stimulated Brillouin Scattering (SBS) process
High energy SBS pulse compression setup and results
Current UV source performance and its limitation
On-going work
Summary

## Slide 3: Project Goal
Opt. Comm. 281, 3356-3360(2008), O. Chalus, A. Sukhinin, A. Aceves, J.-C. Diels
(μm)
(μm)
360 μm
Goal: Reliable UV source with 1GW peak power
Simulation: ns single UV filament propagates up to 100s of m in air.
PRA, 65, 013806 (2001), J. Schwarz and J.-C. Diels

## Slide 4: UV filament source
Nd:YAG laser system
7J/pulse, 10ns, 1.25Hz @1064nm
1GW @266nm
5J/pulse, 5ns, 1.25Hz
70% conversion efficiency from 1064nm to 266nm is impossible!!!
OSC
Amp1
Amp2
Amp4
Amp3
Amp5&6
Seeder

## Slide 5: UV filament source
Nd:YAG laser system
7J/pulse, 10ns, 1.25Hz @1064nm
1GW @266nm
0.1-1J/pulse, Sub-ns, 1.25Hz
Pulse compressor with relatively high energy conversion efficiency
OSC
Amp1
Amp2
Amp4
Amp3
Amp5&6
Seeder

## Slide 6: Physical picture of pulse compression through SBS process
Pump:
Stokes:
z=L
z=0
Acoustic
wave
z
Electrostriction
Two beam interference
[1] R. Boyd, Nonliner Optics 3rd edition, Academic Press 2008
[2] D.T. Hon, Opt. Lett. 5,516-518 (1980)
[3] C. Brent Dane, W. A. Neuman, and L.A. Hackel, IEEE J. Quan. E. 30, 1907(1994)
Positive
feedback
SBS medium
Compressed pulse
Pulse compression
SBS
Input pulse
Transmitted pulse
Time
Distance

## Slide 7: 100% Single axial mode operation with new cavity control method
Single longitudinal and transverse mode operation of the laser system is a prerequisite for pulse compression by Stimulated Brillouin Scattering process

## Slide 8: SBS medium selection for high energy pulse compression
SBS occurs in all states of matter: gases, liquids, solids and plasmas
Liquid is more appropriate for high power application

## Slide 9: SBS setup for high energy pulse compression
HW: Half wave plate QW: Quarter wave plate TFP: Thin film polarizer
f: Focal lens Ls: Generator length La: Amplifier length
Scalable to high energy>1J
With controllable seed energy and timing
Depleted
pump
[1] C. Brent Dane, W. A. Neuman, and L.A. Hackel, IEEE J. Quan. E. 30, 1907(1994)

## Slide 10: High energy SBS compression results
10ns pulse has been compressed to 670ps
Overall efficiency of 73.5% has been achieved
Peak power has been increased 11 times
XiaozhenXu, ChengyongFeng, and Jean-Claude M. Diels. High energy pulse compression through two-pulse interaction mediated by stimulated brillouin scattering in liquid uorocarbon. In CLEO: 2013, page CM3L.4. Optical Society of America, 2013.

## Slide 11: UV laser system
10ns pulse width, 1J energy @1064nm
670ps pulse width, 730mJ energy @1064nm
670ps pulse width, 3.7J energy @1064nm
FWHM:
670ps
FWHM:
10ns

## Slide 12: UV laser system
UV peak power @ 500-600MW
New KDP crystal 50*50*10mm could push this close to 1GW

## Slide 13: Current UV source limitation: Aberration from amplifier cell
Generator-Amplifier setup gains the advantage of high energy capacity but also looses the phase conjugation property

## Slide 14: Current UV source limitation : Aberration from amplifier cell

## Slide 15: Pulse compression in water
[1] G. Abbate, et al. The temperature dependence of the refractive index of water. J. Phys. D: Appl. Phys. 11, 1167 (1978)
Notes: Heavy water in list as backup
2nd version water cell picture

## Slide 16: Pulse compression in water
[1] A. C. Tam, et al. Optical absorptions of light and heavy water by laser optoacoustic spectroscopy. Appl. Opt.. 18, 3348 (1979)
Distilled water
2” OD
2.5 m
Cooling Liquid
2.75” ID
2.7 m
Cooling Liquid
Distilled water
2.5 m
Ver. 1.0
Ver. 2.0
Notes: Heavy water in list as backup
2nd version water cell picture

## Slide 17: Pulse compression in water: Single cell setup
TFP
QW
M
M
CCD
Wedge
BIPLANAR PHOTOTUBE
Hamamatsu R1328U-52
Input beam

## Slide 18: Pulse compression in water: @ room temperature
SBS reflectivity saturates around 72%
Compressed pulse goes below the phonon lifetime of 295ps
The pulse width could be even shorter after the amplification stage

## Slide 19: Pulse compression in water: Distortion free test
Input profile before SBS cell
Profile at 7m away from the exit of SBS cell
Laser pointing stability

## Slide 20: On-going work
New LBO (13.5*13.5*12.5mm)  3J, 10ns @532nm
Water @40C  2J, 250ps @532nm
New KDP (50*50*10mm)  300mJ 200-250ps @266nm
1 GW peak power 266 nm source, generate and study sub-ns UV filament!

## Slide 21: Summary
We developed a new method for stable single axial mode operation of an injection seeded Nd:YAG laser at low repetition rate
We investigated pulse compression through SBS process with generator-amplifier setup both theoretically and experimentally
We realized a UV source with sub GW to 1 GW peak power but also found its limitation in application of filament research
We did preliminary pulse compression experiments in Water and confirmed its better spatial and temporal performance

## Slide 22: What’s important in this setup: 1) Interaction length/timing control
Delay 1: Stokes seed comes
too late---Lower efficiency
(b) Delay 2: Stokes seed comes
at the right time---Perfect
(c) Delay 3: Stokes seed comes too early---Effective
interaction length becomes shorter such that
amplified Stokes peak power decreases and
more energy goes to pulse tail
Notes: What’s important in this setup:1) Interaction length: timing control

## Slide 23: What’s important in this setup: 2) Beam size control
The magnification of 1.31 has been chosen to adapt limited optics size as well as the laser configuration
Notes: What’s important in this setup:2) beam sizecontrol
Seed taking away
Brillouin scattering from pump

## Slide 24
(a) Es=8mJ,ET=60mJ
(b) Es=40mJ, ET=550mJ
(c) Es=40mJ, ET=1010mJ